## Slide 1: 7.Communication
DR.Somsin THongkrairat

## Slide 3: Connectivity
When two or more MCU are in the same system.
Communication are need!

## Slide 4: Simplest communication
Send 1 bit or 1 state at a time (GPIO)
GPIOA 12
GPIOC 5

## Slide 5: Type of communication
Categorize by direction
  Simplex
  Half duplex
  Full duplex
Categorize by topology
  Master-slave
  One-to-one
  broadcast
Categorize by Clock
  Synchronous (Time base)
  Asynchronous (clock base)
LAN
GSP
UART
USART
SPI
I2C
One-wire-Serial
?

## Slide 6: Categorize by direction
  Simplex -> ส่งข้อมูลทางเดียว ไม่สามารถส่งข้อมูลกลับได้
  Full duplex -> ส่งข้อไปกลับพร้อมกันได้
  Half duplex -> ส่งข้อไปกลับ แต่ทำพร้อมกันไม่ได้
A
B
A
B
A
B
Simplex
Half-Duplex
Full-Duplex

## Slide 7: Categorize by topology
  One-to-one -> only 2 MCU in network
  Master-slave -> Master device control communication BUS
  BUS -> every device do same behavior
A
B
One to One
M
S1
Master slave
S2
S3
A
B
BUS
C

## Slide 8: Categorize by Clock
  Synchronous (Time base) -> speed define by time (pre-define)
  Asynchronous (clock base) -> speed define by clock signal (data send with clock signal)
A
B
Asynchronous
data
9600 data per sec
A
B
Synchronous
data
Clock

## Slide 9: STM availability
Serial -> UART -> Asynchronous , FULL-Duplex
SPI -> USART -> Synchronous , Master slave, Half-Duplex
I2C -> Two Wire -> Synchronous , Master slave , Full-Duplex
CAN -> CAN interface -> Asynchronous , BUS, Half-Duplex
UCPD -> Asynchronized
ETH -> LAN

## Slide 10: Serial communication
send serial data through media directory
‘H’ -> 0b01001000 (MSB)
Tx = Transmitter (ตัวส่ง)
Rx = Receiver (ตัวรับ)

## Slide 11: Serial communication data
LSB (less significant bit first) format (Default)
Start bit -> start signal to receive incoming data (logic 0 by default)
Stop bit -> mark end of 1 data (e.g., end of byte) (logic 1 by default)
Parity bit -> check sum (transmit error checking)

## Slide 12
‘H’ -> 0b01001000 (MSB)

## Slide 13: Serial communication
Baud rate = 10000 bps, Start bit = 1 baud, Stop bit = 1 baud
‘H’ -> 0b01001000 (MSB)

## Slide 14: UART
Full duplex , One-to-one , Asynchronous
Rx connect to Tx
Tx connect to Rx
Same baud rate

## Slide 15: Serial (UART) variant
RS232 -> convert logic level to positive and negative (-5V -> 1 , 5V -> 0) or (-15V -> 1 , 15V -> 0)
Improve robustness (longer and faster)
https://en.wikipedia.org/wiki/RS-232#/media/File:Rs232_oscilloscope_trace.svg

## Slide 16: Serial (UART) variant
RS485-> using differential logic () but Half duplex , BUS
*MAX485 datasheet
https://en.wikipedia.org/wiki/RS-485#/media/File:RS-485_waveform.svg

## Slide 17: Serial (UART) variant
RS422-> Full duplex version of RS485 (add 1 pair of wire)
*MAX485 datasheet
https://en.wikipedia.org/wiki/RS-485#/media/File:RS-485_waveform.svg

## Slide 18: Communication programming sender
Sender is easy because device can send when every they want! (LAB1)
Set PC 13 to Input
Setup USART 1 in Asynchronous mode
Set baud rate to 10000 Bps (8bit)

## Slide 19: LAB1
/* USER CODE BEGIN 3 */
unsigned char data[10] = "A"; // = 65 DEC , 0X41 , 0b01000001
while(HAL_GPIO_ReadPin(GPIOC, GPIO_PIN_13) == 0){
HAL_UART_Transmit(&huart1, data, 1, 1000);
data[0]++;
HAL_Delay(3000);
}
HAL_Delay(1000);
}
/* USER CODE END 3 */
Send data when button pressed and increase data 1 when hold button

## Slide 20: Seeing the data
Oscilloscope
Measure data using Oscilloscope
USART1 TX -> PC4 (D1 Arduino)
Then hold button
PC4 (D1 Arduino)

## Slide 22: Serial Receiver
Sender is easy because device can send when every they want! (LAB1)
Receive is more complex because ,We don’t know when the data will come. (LAB2)
Setup USART 1 in Asynchronous mode
Set baud rate to 10000 Bps (8bit)
Sender
Receiver
PC4 (D1)
PC5 (D0)
GND
GND
*Don’t forget to connect GND

## Slide 23: Lab 2 coding
/* USER CODE BEGIN 3 */
unsigned char data[20] = "XXXXXX";
HAL_UART_Receive(&huart1, data, 6, 10000); // blocking receiving
HAL_UART_Transmit(&huart2, data, 6, 1000); // print out to console
HAL_UART_Transmit(&huart2, "\r\n", 2, 1000); // ending line
HAL_GPIO_TogglePin(LED_GREEN_GPIO_Port, LED_GREEN_Pin);
HAL_Delay(1000);
}
/* USER CODE END 3 */

## Slide 24: LAB2 blocking mode
Wait 10 sec every display
Wait 10 sec or got data more then 6 byte
Print data

## Slide 25: LAB 3 interrupt mode
Setup USART 1 in Asynchronous mode
Set baud rate to 10000 Bps (8bit)
Enable interrupt (both USART1 AND USART2)

## Slide 26: LAB 3 interrupt mode
/* USER CODE BEGIN 4 */
void HAL_UART_RxCpltCallback(UART_HandleTypeDef *huart)
{
if(huart == &huart1){
HAL_UART_Transmit_IT(&huart2, data, 8);
HAL_UART_Receive_IT(&huart1, data, 6);
}
}
/* USER CODE END 4 */
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
/* USER CODE END WHILE */
/* USER CODE BEGIN 3 */
HAL_GPIO_TogglePin(LED_GREEN_GPIO_Port, LED_GREEN_Pin);
HAL_Delay(1000);
}
/* USER CODE END 3 */
/* USER CODE BEGIN 0 */
unsigned char data[10] = "XXXXXX\r\n";
/* USER CODE END 0 */

## Slide 27: LAB 3 interrupt mode
void HAL_UART_RxCpltCallback(UART_HandleTypeDef *huart)
{
}
Called when received all byte
Non - blocking

## Slide 28: SPI
Serial but Synchronous and Master – Slave topology.
MOSI -> Master out SLAVE in
MISO -> MASTER in SLAVE out
SCK -> Clock signal from MASTER
CE -> chip select (select chip to communicate)

## Slide 29: LAB4 SPI (MASTER)
Set USART1 to Synchronous Master (10000 bps) , Enable Clock Last bit
Set PD9,PD8 to GPIO output ,PC13 to input

## Slide 30: LAB4 SPI (MASTER)
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
/* USER CODE END WHILE */
/* USER CODE BEGIN 3 */
if(HAL_GPIO_ReadPin(GPIOC, GPIO_PIN_13) == 0){
HAL_GPIO_WritePin(LED_GREEN_GPIO_Port, LED_GREEN_Pin, 0);
HAL_GPIO_WritePin(GPIOD, GPIO_PIN_8, 1);
HAL_USART_Transmit(&husart1, data, 1, 1000);
HAL_GPIO_WritePin(GPIOD, GPIO_PIN_8, 0);
}
else{
HAL_GPIO_WritePin(LED_GREEN_GPIO_Port, LED_GREEN_Pin, 1);
HAL_GPIO_WritePin(GPIOD, GPIO_PIN_9, 1);
HAL_USART_Transmit(&husart1, data, 1, 1000);
HAL_GPIO_WritePin(GPIOD, GPIO_PIN_9, 0);
}
HAL_Delay(500);
data[0]++;
if(data[0] > 'Z'){
data[0] = 'A';
}
}
/* USER CODE END 3 */
/* USER CODE BEGIN 2 */
unsigned char data[10] = "A";
HAL_GPIO_WritePin(GPIOD, GPIO_PIN_8, 0);
HAL_GPIO_WritePin(GPIOD, GPIO_PIN_9, 0);
/* USER CODE END 2 */

## Slide 31: LAB5 SPI (Slave)
Set SPI1 to Full-Duplex Slave
Set 8 bit LSB
Enable SPI1 and UART2 Interrupt
*not necessary to assign baud rate why?

## Slide 32: LAB5 SPI (Slave)
/* USER CODE BEGIN 0 */
unsigned char data[10] = "a\r\n";
/* USER CODE END 0 */
/* USER CODE BEGIN 2 */
HAL_SPI_Receive_IT(&hspi1, data, 1);
/* USER CODE END 2 */
/* USER CODE BEGIN 4 */
void HAL_SPI_RxCpltCallback(SPI_HandleTypeDef *hspi)
{
if(hspi == &hspi1){
HAL_UART_Transmit_IT(&huart2, data, 3);
HAL_SPI_Receive_IT(&hspi1, data, 1);
}
}
/* USER CODE END 4 */

## Slide 33: LAB 4 & 5 Topology
Baud rate is defined by master

## Slide 35: I2C
SPI but use address in communication to select chip (use only 2 wire)
SDA -> DATA
SCL -> CLOCK
Address was assigned to every device except master
Select slave by address

## Slide 36: I2C
Connect start by master ask for device xx
If there are device address xx , device will send ACK back to BUS
ACK = acknowledgement = สัญญาณตอบกลับ
NACK = negative-acknowledgement = สัญญาณตอบกลับแบบลบ

## Slide 37: LAB 6 I2C (MASTER)
Enable I2C set standard frequency 100000 Hz
Set address to 0 (MASTER)
Set PC13 to Input

## Slide 38: LAB 6 I2C (MASTER)
Set pullup PA9(SCL) , PA10(SDA)

## Slide 39: LAB 6 I2C (MASTER)
/* USER CODE BEGIN 2 */
unsigned char data[10] = "haruhi";
/* USER CODE END 2 */
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
/* USER CODE END WHILE */
/* USER CODE BEGIN 3 */
if(HAL_GPIO_ReadPin(GPIOC, GPIO_PIN_13) == 0){
HAL_GPIO_WritePin(LED_GREEN_GPIO_Port, LED_GREEN_Pin, 0);
HAL_I2C_Master_Transmit(&hi2c1, 0x03 << 1, data, 6, 1000);
}
else{
HAL_GPIO_WritePin(LED_GREEN_GPIO_Port, LED_GREEN_Pin, 1);
HAL_I2C_Master_Transmit(&hi2c1, 0x04 << 1, data, 6, 1000);
}
HAL_Delay(2000);
data[0]++;
if(data[0] > 'z'){
data[0] = 'a';
}
}
/* USER CODE END 3 */

## Slide 40: LAB 7 I2C Slave
Enable I2C set standard frequency 100000 Hz
Set address to 0x03 and 0x04
Enable I2C1 and UART2 interrupt

## Slide 41: LAB 7 I2C Slave
Set pullup PA9(SCL) , PA10(SDA)

## Slide 42: LAB 7 I2C Slave
/* USER CODE BEGIN 4 */
void HAL_I2C_ListenCpltCallback (I2C_HandleTypeDef *hi2c)
{
HAL_I2C_EnableListen_IT(hi2c);
}
extern void HAL_I2C_AddrCallback(I2C_HandleTypeDef *hi2c, uint8_t TransferDirection, uint16_t AddrMatchCode)
{
if(TransferDirection == I2C_DIRECTION_TRANSMIT) // if the master wants to transmit the data
{
HAL_I2C_Slave_Sequential_Receive_IT(hi2c, data, 6, I2C_FIRST_AND_LAST_FRAME);
}
else // master requesting the data is not supported yet
{
Error_Handler();
}
}
void HAL_I2C_SlaveRxCpltCallback(I2C_HandleTypeDef *hi2c)
{
if(hi2c == &hi2c1){
HAL_UART_Transmit_IT(&huart2, data, 6);
}
}
void HAL_I2C_ErrorCallback(I2C_HandleTypeDef *hi2c)
{
HAL_I2C_EnableListen_IT(hi2c);
}
/* USER CODE END 4 */
/* USER CODE BEGIN 2 */
HAL_I2C_EnableListen_IT(&hi2c1);
/* USER CODE END 2 */
/* USER CODE BEGIN 0 */
unsigned char data[10] = "A\r\n";
/* USER CODE END 0 */

## Slide 43: I2C topology