## Slide 1: 4.EEPROM (Non-volatile memory)
DR.Somsin THongkrairat

## Slide 3: EEPROM
ROM -> read-only memory
PROM-> programmable read-only memory
EPROM-> erasable programmable read-only memory
EEPROM-> electrically erasable programmable read-only memory

## Slide 4: Where are code stored in MCU
Yes memory , Which one?
*From rm0444 page 56
A. CPU
B. RAM
C. FLASH
D. All above
A
B
C

## Slide 5: MEMORY
Register (in CPU) -> define peripheral behavior and process
RAM -> store variable and HEAP
FLASH -> store program (code) and persistence memory

## Slide 6: What is persistence memory
- อะไรก็ตามที่คงสถานะ (state) ไว้ได้ถึงแม้ว่าจะไม่มีแหล่งจ่ายไฟ (aka. non-volatile memory , ROM)

## Slide 7: Uploading code
That why our program are persistence (we can plug off and plug in USB without reuploading code)
เป็นเหตุผลว่าทำไมโปรแกรมเรายังอยู่ใน MCU ในเมื่อเราหยุดจ่ายไฟให้ MCU

## Slide 8
Our Code (in binary)

## Slide 9: Compare RAM and FLASH(ROM)
comparation | RAM | FLASH
Speed | Super fast | fast
Persistence | NO | YES
Write Cycle | unlimited | Limited (10k – 1M cycle)
Price | More Expansive | Expansive
Size usually vary with price (want more pay more!)

## Slide 10: Using RAM
- count number of released button and store in variable
Set PC13 to input

## Slide 11: Coding
4_1_button_counter
/* USER CODE BEGIN 2 */
long but_release_count;
unsigned char string_buffer[50];
int string_buffer_size = -1;
int last_button_state = HAL_GPIO_ReadPin(GPIOC, GPIO_PIN_13);
int button_state;
/* USER CODE END 2 */
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
button_state = HAL_GPIO_ReadPin(GPIOC, GPIO_PIN_13);
if(last_button_state == 0 && button_state == 1){ // release
but_release_count++;
string_buffer_size = sprintf(string_buffer,"haruhi %ld\r\n",but_release_count);
HAL_UART_Transmit(&huart2, string_buffer, string_buffer_size, 1000);
HAL_Delay (200); // debounce
}
last_button_state = button_state;
HAL_Delay (100);
/* USER CODE END WHILE */
/* USER CODE BEGIN 3 */
}
/* USER CODE END 3 */
Reset
Reset

## Slide 12: Why variable reset after MCU reset?
It on RAM, not persistence memory.
ตัวแปรอยู่บน RAM ไม่ได้อยู่บน persistence memory
but_release_count
How to make it count continuedly (after Reset) ?
ทำอย่างไรให้ MCU นับต่อไป (หลังจาก Reset) ?

## Slide 13: How to store data persistency
- Write data to file system (SD card , flash drive)
- Send data to network and load
- Use external memory (external FLASH)
- Use internal memory (FLASH)

## Slide 14: EEPROM
electrically erasable programmable read-only memory
A type of Device or memory the provide non-volatile memory user can read and reprogram each byte on memory repeatedly.
คือ ประเภทของอุปกรณ์ หรือ หน่วยความจำ (memory) ที่สามารถอ่านและเปลี่ยนแปลงข้อมูลได้ เรื่อย ๆ โดยสามารถคงสถานะได้แม่จะไม่มีแหล่งจ่ายไฟ (non-volatile)

## Slide 15: EEPROM chip
AD24C02 (2K bits[256*8])
Memory
Write cycle 1M cycle
Store time 100 year?
24LC01B/02B (2Kbits [256*8])

## Slide 16: EEPROM Emulator
- using FLASH as EEPROM , ใช้พื้นที่บน FLASH memory แต่ใช้แบบ EEPROM
Emulate to EEPROM

## Slide 17: How to use EEPROM (write)
H
A
R
U
H
I
Write(PAGE,ADDR,DATA)
Write(0,0,’H’)
Write(0,1,’A’)
Write(0,2,’R’)
Write(0,3,’U’)
Write(1,0,’H’)
Write(1,1,’I’)
Writable memory indexing by address
สามารเขียนข้อมูลไปยัง address ได้

## Slide 18: How to use EEPROM (Read)
H
A
R
U
H
I
Read(PAGE,ADDR)
Read(0,0) -> ‘H’
Read(0,1) -> ‘A’
Read(0,2) -> ‘R’
Read(0,3) -> ‘U’
Read(1,0) -> ‘H’
Read(1,1) -> ‘I’
Readable memory using address
สามารอ่านข้อมูลอ้างอิงโดย address

## Slide 19: EEPROM on CUBE ide
Set PC13 to input
Just for button
(not relate to EEPROM)
Enable CRC for EEPROM

## Slide 20: EEPROM on CUBE ide
Copy into Driver Folder
Right Click
Click Refresh to refresh library and reindexing

## Slide 21: Config Environment
Right Click
Select Properties
Add include Path
1
2
3

## Slide 22: coding
/* USER CODE BEGIN Includes */
#include "eeprom_emul.h"
/* USER CODE END Includes */
Init EEPROM Emulator (select PAGE 16)
Unlock Flash to Writable Mode
Write EEPROM
Read EEPROM

## Slide 23
/* USER CODE BEGIN 2 */
HAL_FLASH_Unlock();
/* EEPROM Init */
HAL_Delay(2000);
EE_Init(EE_FORCED_ERASE);
unsigned char string_buffer[50];
int string_buffer_size = -1;
HAL_UART_Transmit(&huart2, (uint8_t *)"haruhi\r\n", 8, 1000);
if(HAL_GPIO_ReadPin(GPIOC,GPIO_PIN_13) == 0){ // If User Button is Pressed the Write EEPROM
char write_word[20] = "hatsune miku\r\nr";
for(int i=0;i<15;i++){
EE_WriteVariable8bits(20 + i, write_word[i]);
}
}
/* USER CODE END 2 */
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
// read data from eeprom
EE_ReadVariable8bits(20, &string_buffer[0]);
EE_ReadVariable8bits(21, &string_buffer[1]);
EE_ReadVariable8bits(22, &string_buffer[2]);
EE_ReadVariable8bits(23, &string_buffer[3]);
EE_ReadVariable8bits(24, &string_buffer[4]);
EE_ReadVariable8bits(25, &string_buffer[5]);
EE_ReadVariable8bits(26, &string_buffer[6]);
EE_ReadVariable8bits(32, &string_buffer[7]);
EE_ReadVariable8bits(33, &string_buffer[8]);
//string_buffer_size = sprintf(string_buffer,"%s",string_buffer);
string_buffer_size = sprintf(string_buffer,"%c%c%c%c%c%c%c%c",string_buffer[0],string_buffer[1],string_buffer[2],string_buffer[3],string_buffer[4],string_buffer[5],string_buffer[6],string_buffer[7]);
HAL_UART_Transmit(&huart2, string_buffer, string_buffer_size, 1000);
HAL_Delay (1000);
/* USER CODE END WHILE */
/* USER CODE BEGIN 3 */
}
/* USER CODE END 3 */

## Slide 24: Warning
Always use delay 500 – 1000 ms
ให้ใส่ delay 500 – 1000 ms เสมอ
Because it is limited cycle to write (prevent write in same address rapidly)
เพื่อป้องกันการเขียนซ้ำที่เดิมเป็นจำนวนมากครั้ง เนื่องจากจะทำให้ Flash address นั้นพัง

## Slide 25: Result
Reset
Write to EEPROM

## Slide 26: Function
EE_Status EE_WriteVariable8bits(uint16_t VirtAddress, uint8_t Data)
EE_Status EE_ReadVariable8bits(uint16_t VirtAddress, uint8_t* pData)
Write [Data] at memory address [VirtAddress]
Read memory at [VirtAddress] and store in [pData]
บันทึก [Data] ไปยัง [VirtAddress]
อ่านข้อมูลจาก address [VirtAddress] และนำไปเก็บไวที่ pData

## Slide 27: LAB
ทำให้ button counter นับต่อไปถึงแม้ว่าจะถอด USB และ เสียบใหม่ก็ตาม
ทำต่อจากไฟล์ LAB3 ได้
Reset
Remove and Plugin USB
Reset